## Slide 1: Time Integration of Reacting Flows and Energy-Stable Hybrid Spatial Discretizations
Cory Mikida (AE)
Prof. Daniel Bodony (AE)
Prof. Andreas Klockner (CS)

## Slide 2: The Topic/Problem
Ablation test (VKI)
The mission statement: develop stable, accurate, and efficient multi-rate time integration schemes for reacting flows
In these equations:
𝜌 = density
ui = velocity in ith direction
𝛿ij = Kronecker delta
𝜏ij = fluid stress tensor
E = total energy
T = temperature
P = pressure
q = heat flux
Wk = molecular weight of kth species
ὠk = production rate of kth species
R = gas constant
n = number of moles of gas
[C]k = concentration of kth species
Cv,k = specific heat at constant volume of kth species
Uk(T) = internal energy of kth species at temperature T
Yk = mass fraction of kth species
𝜑ki = diffusion flux of kth species

## Slide 3: The Topic/Problem
Ablation test (VKI)
The mission statement: develop stable, accurate, and efficient multi-rate time integration schemes for reacting flows
Cons. of mass
Cons. of momentum
Cons. of energy
Time derivative of ideal gas law
Derived from constant internal energy assumption
Species mass fraction equation
Navier-Stokes

## Slide 4: The Topic/Problem
Ablation test (VKI)
The mission statement: develop stable, accurate, and efficient multi-rate time integration schemes for reacting flows
Chemical source terms in governing equations tend to be stiff, setting the limiting timestep to be oppressively low relative to the fluid motion or requiring implicit treatment
Research Question: Can we derive performance benefit from using multi-rate Adams integrators?
Species production rates (stiff)

## Slide 5: Goals and Bounds
Ablation test (VKI)
Must-have: demonstrate a novel scheme (adaptive implicit-explicit multi-rate) driving a canonical or demonstrative reacting flow problem (more) correctly and (more) efficiently
  Current candidate problem: reacting mixing layer
  See planning slides for more detail on this problem
Must-have: monitor and maintain presence of solution on constraint manifold (ideal gas law)
  Fully differential approach to satisfying constant volume/constant internal energy assumptions can produce nonphysical solutions
  Potential mitigation approaches: modified Jacobian to incorporate algebraic constraints, kinetic RHS attenuation (DAEs)

## Slide 6: Goals and Bounds (cont’d)
Ablation test (VKI)
Nice-to-have: report on and/or optimize time integration within design space provided by multi-rate framework
  Adaptivity choices (see next slide)
  Evaluation order (”fastest-first” vs. ”slowest-first”, etc.)
  Re-extrapolation?
  Inclusion of additional history (shown in [1] to improve stability/timestep restrictions)
Nice-to-have: demonstrate tangible improvement over CVODE (state of the art) in at least one metric
  Temporal order of accuracy, specifically when coupled with fluid solver
  Number of chemistry RHS calls required to reach end time – proxy for performance improvement beyond simple walltime measurement
Beyond our bounds: multivariable solves incurred by certain situations (multiple coupled implicit RHSs, IMEX LTE)

## Slide 7: The Plan
Implement multi-rate Adams integrators (established as a viable vehicle for performance improvement by [1])
  Add ability to integrate chemistry implicitly, and at a different timestep than that of the fluid motion
  Coupling the chemistry with the fluid RHS will elevate temporal accuracy beyond that of the previous splitting approach (first order)
  Timestep adaptivity also identified as critical need in early testing – add this capability to multi-rate Adams integration using local error estimates as with ODE45/CVODE
r >= 1
r < 1
q = order
sq = state estimate obtained via explicit scheme of order q

## Slide 8: The Plan (cont’d)
Adding adaptivity based on error estimates also introduces a number of design choices to be explored
Timestep adaptivity versus step ratio adaptivity
  Incurs long-standing software research question of generating variable step-ratio multi-rate code
  Step ratio adaptivity would make constant-timestep runs with error control possible, provided the fast component dominates overall error
  Error control mechanism based on step ratio alteration may prove to be more efficient
Track local error/make adaptivity decisions based on subset of solution components?
  Fast-evolving solution component (species mass fractions) may dominate local error
  Confirming this would allow us to reduce overhead in terms of both memory and cost by refraining from tracking the slow component

## Slide 9: The Plan (cont’d)
Application: demonstrative reacting mixing layer problem
  Hyperbolic tangent velocity profile as baseflow ([2], [3])
  San Diego 9-species chemical mechanism
  Initial condition: introduce temperature variation to localize autoignition to the mixing layer
This problem is suitable for our uses in that it provides multiple turnable ”knobs” for changing the rates of the fluid vs. the chemical kinetics, and vice versa
  Scale magnitude of hyperbolic tangent velocity profile
  Scale species production rates by altering reaction Arrhenius rates

## Slide 10: The Plan (cont’d)
Application: demonstrative reacting mixing layer problem
  Hyperbolic tangent velocity profile as baseflow ([2], [3])
  San Diego 9-species chemical mechanism
  Initial condition: introduce temperature variation to localize autoignition to the mixing layer
This problem is interesting and physically useful in that it provides the simplest relevant model of combustion in a scramjet/ramjet

## Slide 11: Impact
Ablation test (VKI)
Software: development of additional integration schemes within Leap/Dagrt framework, additional PyJac-V2 development
  NASA9 thermodynamic polynomial descriptions already implemented in PyJac-V2 as added feature
Broader Impact: improved time-to-solution at high order for reacting flow problems
  Subsonic/supersonic combustion for propulsion: gas turbines, scramjets/ramjets, rockets
  Furnaces/residential heating
  Atmospheric sciences

## Slide 12: Risk Mitigation
Ablation test (VKI)
Important question: what if this doesn’t work out?
  Reinforces CVODE as state-of-the-art for implicit treatment of chemical kinetics
  However, a ”fallback” of sorts would be demonstrating a higher degree of temporal accuracy in the coupled fluid problem using a Leap-generated IMEX approach with PyJac-generated Jacobians
  Given that these Jacobians are not finite difference, and given that this eliminates the splitting scheme currently employed (at best first-order), I’m much more confident in this as a preliminary outcome
Is this ”fallback” outcome interesting enough?
  If so, should proving this (showing first order in splitting approach and higher-order with Leap RK approach on a demonstrative problem) be the initial goal?
  If not, what is left?

## Slide 13: Current Status
Ablation test (VKI)
Leap RK IMEX integration built into PlasCom2, using PyJac-generated chemical Jacobian for implicit solve
  PyJac modified to include NASA9 thermodynamic polynomials (useful/required for maintaining accuracy for ignition problems with large temperature ranges)
Adams-Moulton integrators implemented as baseline for implicit treatment of chemistry in multi-rate Adams
  Working its way through code review
Error-informed timestep adaptivity incorporated into single-rate and multi-rate Adams integrators
  Local error estimate formed using explicit methods of differing orders
  Multi-rate implementation needs to be tested w/stiff problem

## Slide 14: Current Status (cont’d)
Ablation test (VKI)
Implicit-explicit multi-rate w/adaptivity in development
Fluid solver requires incorporation of mass diffusion terms in governing equations
Reacting mixing layer in development (demonstrative case)
  Currently struggling to stand up simulation
  As of 12/28, cold flow case with unstable mode as initial condition is running
  This is functioning to eyeball norm, but growth rate/physics need to be verified before introducing temperature variation/ignition
  Whether the unstable mode still provides a good initial condition in the reacting case is unclear and needs to be determined
One-dimensional premixed laminar flame
  Functioning as a baseline case to compare reacting fluid solver’s estimated laminar flame speed with steady-state analysis (Cantera)

## Slide 15: The Topic/Problem
Ablation test (VKI)
The mission statement: create a stable and accurate interface between structured (SBP) and unstructured (DG) spatial discretizations
  Introducing localized regions of unstructured meshing allows for superior meshing of complex geometries
  Most approaches to this present in literature appear to have at most second-order accuracy
  Few approaches provide any claims about stability
Image credit: “A hybrid FETD-FDTD method with nonconforming meshes”, Zhu et. al

## Slide 16: The Topic/Problem
Ablation test (VKI)
Starting point: nonconforming interface method of Kozdon and Wilcox ([4])
  Boundary between spatial schemes traversed via projection of solution into “glue grid” polynomial space
  Choice of polynomial space in glue grid/structure of projection operators can allow for proof of energy stability
  However, resulting projection stencils give an underdetermined system, with optimization used to produce final projection operators
Illustration of glue-grid method in traversing nonconforming SBP-to-SBP boundaries.

## Slide 17: The Topic/Problem/Impact
Ablation test (VKI)
Research Question: can we make stability guarantees in a manner similar to this work while avoiding ad-hoc/optimization-based approach to operator construction?
Draft theorem to prove: If a function defined on a finite-difference mesh is coupled to an unstructured mesh via a nonconforming interface, the coupling is stable and accurate to order q provided the projection operators from finite-difference to unstructured (and vice versa) satisfy condition X.
Broader Impact: improved flexibility in modeling fluid problems with complex geometries
  Provide alternative to overset/multiblock curvilinear meshing for such problems
  Locally introduce shock-handling benefits of DG into previously finite-difference-only simulations with relative ease

## Slide 18: Goals and Bounds
Ablation test (VKI)
Must-have: stable, accurate, and *unisolvent* approach to interior projection from structured (SBP) to unstructured (DG) meshes in 2D
  Unisolvent: same number of unknowns (DOFs) as constraint equations
  Seek one-to-one projection: round trip across interface does not result in data loss
  Apply this to a periodic problem as a baseline proof-of-concept
Nice-to-have: application to 3D problems
Nice-to-have but based on our current experience will be tricky: stable, accurate, and unisolvent boundary projection
  Boundary stencils are currently what make the whole-operator solves of Kozdon and Wilcox underdetermined

## Slide 19: The Plan
Ablation test (VKI)
Starting point: remove more complicated boundary treatment from setup, construct interior-only periodic projection operators
  Be able to write down time-continuous proof of stability (via energy) - this may result in a different operator condition than K+W’s compatibility, and may require a more thorough search for all possible operator conditions than has yet been performed
  Establish a sensible set of DOFs
  Solve for these operators from a square system based on accuracy conditions for projection in *both* directions (grid-to-glue, glue-to-grid), in addition to any constraints we need to impose to ensure stability (based on conditions mentioned above)

## Slide 20: The Plan (cont’d)
Ablation test (VKI)
Prove the efficacy of these projection operators in 2D
  Demonstrate code that solves set of constraint equations for set of unknowns to produce projection operators (and provide as electronic supplement)
  Practically demonstrate order of accuracy of projection across interface using L2 error
  Numerically demonstrate non-increasing energy on demonstrative problem, and compare numerically observed energy rate-of-change to that derived by the energy stability proof
Apply lessons learned to boundary treatment

## Slide 21: The Plan (cont’d)
Ablation test (VKI)
Application: 2D acoustic wave equation on split domain

## Slide 22: Risk Mitigation
Ablation test (VKI)
Important question: what if this doesn’t work out?
  Can try to establish more concretely why Kozdon and Wilcox’s underdetermined result is truly the best one for our purposes while highlighting suspect error behavior at boundary
  Can attempt to extend this method to 3D (not done in their paper/unclear what challenges this could potentially pose)
  Can also determine whether there is a timestep limitation imposed by Kozdon and Wilcox’s method, and – if so – attempt to expose the coupling to multi-rate for performance improvement
Is this ”fallback” outcome interesting enough?
  If not, what is left?

## Slide 23: Current Status
Ablation test (VKI)
Python-based testing setup created which implements split-domain 2D acoustic wave problem described on the previous slide
  SBP-side boundary fluxes incorporated into DG software package
  Energy stability verified with Kozdon and Wilcox’s operators via comparison of numerically observed energy rate-of-change and that used in their energy stability proof
Matlab and Maxima codes written with the goal of experimenting with different DOF/constraint setups to produce a unisolvent and stable interior projection operator
  Needed: firmer understanding of how compatibility condition of K+W fulfills interior projection operator accuracy constraints in both directions (pencil and paper)
  Needed: experimentation with alternatives to compatibility condition – how to find out whether any other suitable operator conditions exist?

## Slide 24: References
Ablation test (VKI)
[1] Mikida, Cory, Andreas Klöckner, and Daniel Bodony. "Multi-rate time integration on overset meshes." Journal of Computational Physics 396 (2019): 325-346.
[2] Michalke, Alfons. "On the inviscid instability of the hyperbolictangent velocity profile." Journal of Fluid Mechanics 19.4 (1964): 543-556.
[3] Blumen, William. "Shear layer instability of an inviscid compressible fluid." Journal of Fluid Mechanics 40.4 (1970): 769-781.
[4] Kozdon, Jeremy E., and Lucas C. Wilcox. "Stable coupling of nonconforming, high-order finite difference methods." SIAM Journal on Scientific Computing 38.2 (2016): A923-A952.