## Slide 1: Time Integration of Reacting Flows and Energy-Stable Hybrid Spatial Discretizations
Cory Mikida (AE)
Preliminary Exam (Thursday, February 25th, 2021)

## Slide 2: Goals for This Presentation
Ablation test (VKI)

## Slide 3: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document

## Slide 4: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document
Expound upon certain aspects of both topics, namely current work

## Slide 5: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document
Expound upon certain aspects of both topics, namely current work
More extensively motivate how I hope to spend the “best days of my life”

## Slide 6: Time Integration of Reacting Flows

## Slide 7: Motivation and Background
Ablation test (VKI)
Time integration of chemically reacting flows presents a significant set of simulation challenges
  Presence of stiff terms limits timestep – fluid-relevant timescale is much larger than reaction timescale
  Going fully explicit -> wasteful work
  Going implicit -> restrictive solve requirements
One common approach: operator splitting
What numerical tools exist that allow us to do better?

## Slide 8: Motivation and Background
Ablation test (VKI)
IMEX schemes, e.g. additive Runge-Kutta schemes of Kennedy and Carpenter
  Designed primarily for convection-diffusion-reaction equations
  Higher order (can be lost when simulating DAEs)
  Timestepping limitations removed, but timescales not easily split
Multi-rate schemes, e.g. multi-rate multistep schemes derived from Gear and Wells
  Splitting of timescales comes from per-component history management on different intervals
  Mixing of implicitly and explicitly advanced components not yet accomplished/unexplored

## Slide 9: Motivation and Background
Ablation test (VKI)
Given: an existing framework for multi-rate integration that has been proven effective for fully-explicit time advancement
  Timescale splitting -> apply CFL condition to overset meshes
  Component coupling -> energy-stable penalty-based interpolation
  Implementation: Python packages for code generation of multi-rate integrators as well as a number of other schemes, some of which are implicit/incorporate implicit solves
Consider: combining performance improvement capabilities of multi-rate integration with flexibility of treating different right-hand sides implicitly or explicitly

## Slide 10: Motivation and Background
Ablation test (VKI)
Potential impact: challenge existing state-of-the-art for CFD simulation of reacting flows -> produce faster and more accurate turnaround for…
  Combustion for propulsion: scramjets/ramjets
  Problems in atmospheric sciences -> climate concerns
  Furnaces/residential heating -> energy efficiency

## Slide 11: The Topic/Problem
Ablation test (VKI)
The mission statement: develop efficient, accurate, and stable time integration schemes for reacting flows
  Efficient: splitting of timescales via multi-rate
  Accurate and Stable: high-order temporal resolution, with flexibility to advance separate components implicitly or explicitly, as well as adaptivity introduced via local error-informed timestep control
Gauging efficacy: comparison with existing methods, stress-testing with appropriately stiff demonstrative problems

## Slide 12: Governing Equations
Ablation test (VKI)
Navier-Stokes equations with added equations for mass fraction evolution, as well as pressure/temperature evolution
In these equations:
𝜌 = density
ui = velocity in ith direction
𝛿ij = Kronecker delta
𝜏ij = fluid stress tensor
E = total energy
T = temperature
P = pressure
q = heat flux
Wk = molecular weight of kth species
ὠk = production rate of kth species
R = gas constant
n = number of moles of gas
[C]k = concentration of kth species
Cv,k = specific heat at constant volume of kth species
Uk(T) = internal energy of kth species at temperature T
Yk = mass fraction of kth species
𝜑ki = diffusion flux of kth species

## Slide 13: Governing Equations (2)
Ablation test (VKI)
Primary stiffness contribution is of course from the mass fraction evolution equations – in particular our focus is on RHS
Pressure and temperature updates typically come from energy relation/EOS:
For now, we instead adopt time rate of changes for these quantities based on operator-splitting approach (constant internal energy/volume in reaction substep)

## Slide 14: Gap: Thermodynamic Quantities
Ablation test (VKI)
Various thermodynamic quantities for gas mixtures: NASA 9-coefficient polynomial characterization
  Unlike NASA7, supports arbitrary number of temperature regions
  More accurate in cases with large temperature variation
Used to produce per-species descriptions of internal energy and specific heats at constant volume
Totals for mixtures can be obtained using these quantities in conjunction with species concentrations

## Slide 15: Gap: Mass Diffusion
Ablation test (VKI)
Mass diffusion: mixture-averaged model with correction term for mass conservation
Xk: mole fraction of species k, W: mean molecular weight, Dk,m: binary diffusivity coefficient
How stiff is this relative to the species production rates?

## Slide 16: Gap: Species Production Rates
Ablation test (VKI)
Species production rates: Arrhenius rates

## Slide 17: Numerics: Multi-Rate Integration
Ablation test (VKI)
Solve y’ = a(t,y)…split into fast/slow terms
Multi-step methods: construct an approximation of a, ã based on history of past values
  Adams-Bashforth: construct ã using polynomial interpolation (explicit)
  For multi-rate: each a term in RHS has its own history, speed of evolution
yn+1 obtained by integrating ã
ã

## Slide 18: Numerics: Multi-Rate Integration (2)
Solve y’ = a(t,y)…split into fast/slow terms
Multi-step methods: construct an approximation of a, ã based on history of past values
  Adams-Moulton: construct ã using polynomial interpolation (implicit)
  For multi-rate: each a term in RHS has its own history, speed of evolution
yn+1 obtained by integrating ã
ã

## Slide 19: Numerics: Multi-Rate Integration (3)
Design choices for scheme synthesis include:
  Choice of timescale splitting – which components are fast-evolving, which are slow
  Step ratio
  Evaluation order: “fastest-first” vs. “slowest-first”
  When to re-extrapolate
  How much history to include: stability implication

## Slide 20: Gap: Multi-Rate Example
A walk-through of a macro-step with a simplified system…
Fastest-first scheme, step ratio H/h of 2
Step 1: Form polynomial extrapolants for both right-hand sides

## Slide 21: Gap: Multi-Rate Example (2)
Step 2: Integrate both extrapolants through one microstep
Step 3: Evaluate af at ti+1
Step 4: Update polynomial extrapolant for af to include new history

## Slide 22: Gap: Multi-Rate Example (3)
Step 5: Integrate fast extrapolant through one microstep; integrate slow extrapolant through one macrostep
Step 6: Evaluate af and as at ti+2
Step 7: Update polynomial extrapolants to include new history

## Slide 23: Numerics: Multi-Rate Integration (4)
Summary: reduction in total RHS evaluations is achieved by evaluating fast RHS twice as often as the slow RHS
  The key to the method is maintenance of histories at differing timestep intervals
  Initial histories are obtained via “bootstrapping” with Runge-Kutta methods of matching order
  Pictorial representations of macrostep process given in Kloeckner for a number of different configurations
What about application to chemistry/inclusion of implicit evaluation?

## Slide 24: Numerics: Multi-Rate Chemistry
Ablation test (VKI)
Revisit the governing equations: need to identify fast and slow components and coupling/self-influencing right-hand sides

## Slide 25: Numerics: Multi-Rate Chemistry (2)
With this possible splitting, right-hand side terms become:

## Slide 26: Numerics: Multi-Rate Chemistry (3)
Ablation test (VKI)
This is one possible setup, and its efficacy is currently undetermined
  Timescales of certain components and right-hand sides (energy, mass diffusion) somewhat unknown – mechanism specificity?
  Rates of coupling terms are a design choice to be determined
  Pressure and temperature right-hand sides still predicated upon operator splitting approach – their use will be clarified
Different splittings, step ratios, orders, schema are easily implemented via code generation approach (Leap, Dagrt)

## Slide 27: Numerics: Implicit Chemistry
Ablation test (VKI)
Given the stiffness of the chemistry that motivates this time integrator development, a natural inclusion in our framework is the ability to advance implicitly

## Slide 28: Numerics: Implicit Chemistry
Given the stiffness of the chemistry that motivates this time integrator development, a natural inclusion in our framework is the ability to advance implicitly

## Slide 29: Numerics: Implicit Chemistry (2)
Key need: Jacobian for the chemistry right-hand sides
  CVODE/operator-splitting approach uses a finite-difference Jacobian
  Being able to calculate actual Jacobian may have simulation value
  This motivates the selection of temperature and pressure right-hand sides based on an operator-splitting approach
PyJac-V2: code generation of source terms and Jacobians

## Slide 30: Numerics: Implicit Chemistry (3)
Some important distinctions:
  PyJac-V2 implements equations that assume a reaction substep model, taking either constant-pressure/enthalpy or constant-volume/internal energy
  For the time being we are using the latter
  PyJac-V2 also implements the equations using the number of moles of each species as the independent variables
Constant-Volume
Constant-Pressure

## Slide 31: Numerics: Implicit Chemistry (4)
Critical consideration: ideal gas law drift
  Time-integrating the temperature and pressure differentials no longer rigorously enforce algebraic constraints (constant internal energy, ideal gas law)

## Slide 32: Numerics: Implicit Chemistry (5)
To mitigate this: Jacobian modification
  Removes pressure and temperature rows/columns
  Incorporates constant internal energy constraint into species elements
  Pressure and temperature can then be updated algebraically
Additional option: RHS penalization (attenuation)

## Slide 33: Gap: PyJac-V2 Verification
(Insert text here)

## Slide 34: Numerics: Error/Timestep Control
Motivation: reacting flow simulations, especially featuring ignition, often feature stretches of near-equilibrium chemistry punctuated by temperature/mass fraction spikes
  Timestep requirements for stability/accuracy naturally vary

## Slide 35: Numerics: Error/Timestep Control (2)
Ablation test (VKI)
CVODE accounts for this by obtaining a local truncation estimate using state calculations at two differing orders – we match this approach
  Similar to ODE23/ODE45 timestep adaptors, but uses weighted RMS norm to handle states with components widely varying in magnitude
  State calculations for Adams methods: carry extra history value
|E|>1
|E|<1

## Slide 36: Numerics: Error/Timestep Control (3)
Ablation test (VKI)
Design choices inherent to this approach:
  How often to adapt the timestep (micro- vs. macrostep checks)
  Error norm/adapting controller to stiffness-related situations (later)
  Which state components should be included when
  Timestep adaptivity vs. step ratio adaptivity
|E|>1
|E|<1

## Slide 37: Current Status: Controller
Ablation test (VKI)
Applying fully explicit (adaptive) integration to stiff Cantera example problem to stress-test controller

## Slide 38: Current Status: Controller (2)
Ablation test (VKI)
Applying fully explicit (adaptive) integration to stiff Cantera example problem to stress-test controller
Governing equations do not allow for PyJac intervention
Ablation test (VKI)
Reactor 1
Reactor 2

## Slide 39: Current Status: Controller (3)
Ablation test (VKI)
Applying controller to known methods (namely embedded RK – ODE23) shows timestep “jitter” near chemical equilibrium
  Floating-point issues/cancellation – documented by PyJac
  Use of Scipy implementation confirms this result
  Can we design a controller for integration that alleviates this?
Ablation test (VKI)
Ablation test (VKI)
Leap

## Slide 40: Current Status: Controller (3)
Ablation test (VKI)
Applying controller to known methods (namely embedded RK – ODE23) shows timestep “jitter” near chemical equilibrium
  Floating-point issues/cancellation – documented by PyJac
  Use of Scipy implementation confirms this result
  Can we design a controller for integration that alleviates this?
Ablation test (VKI)
Ablation test (VKI)
Leap
Scipy

## Slide 41: Demonstrative Test Problem
Ablation test (VKI)
Target application: reacting mixing layer
  Fundamentally-driven model of combustion for propulsion
  Twistable speed knobs: crossflow magnitude (fluid), Arrhenius pre-exponential factors (chemistry)
Baseflow: hyperbolic tangent velocity profile
  San Diego 9-species ideal gas mixture
  Ignition localized to mixing layer via introduction of temperature variation

## Slide 42: Current Status: Test Problem
Ablation test (VKI)
Establishing initial perturbation and subsequent growth rate that matches literature using linear stability theory

## Slide 43: Current Status: Synthesis/Verification
Ablation test (VKI)
In the midst of multi-rate Adams development, implicit chemistry framework can be tested with schema existing in Leap
Generate code for chemical source terms, Jacobian, and IMEX ARK4 integration (K+C), and ”wire in” to fluid solver (PlasCom2)
Ensure that we have…

## Slide 44: Current Status: Synthesis/Verification
Ablation test (VKI)
…design-order convergence for a homogeneous autoignition example (9-species San-Diego mechanism) ✓

## Slide 45: Current Status: Synthesis/Verification
Ablation test (VKI)
…good agreement with laminar flame speed returned by steady-state Cantera analysis for a freely propagating flame example✓
To-do: design order convergence in this case?

## Slide 46: Risk Mitigation
Ablation test (VKI)
Important question: what if this doesn’t work out?
  Reinforces CVODE as state-of-the-art for implicit treatment of chemical kinetics
  Fallback: exploration of effect of analytical Jacobian versus finite difference Jacobian. Convergence effects? Performance effects?
  Fallback: controller improvement. Tailoring to kinetics/mechanism?
  Fallback: other target applications for implicit-explicit multi-rate
Actionable response: frontload controller design, Jacobian implementation/verification using simple(r) problems

## Slide 47: Outlook and Open Questions
Ablation test (VKI)
Quantifiably characterizing benefit of analytical versus finite-difference Jacobian
  Accuracy and time-to-solution (fewer implicit solve iterations)
  Rigorously test effect(s) of constant-volume assumption for Jacobian
Develop error/timestep control algorithm with more robustness in the face of near-equilibrium floating point issues
Establish timescale splitting for full governing equations
Explore (large) design space
  Implicit-explicit multi-rate framework
  Timestep control algorithm also has “knobs” to turn

## Slide 48: Energy-Stable Hybrid Spatial Discretizations

## Slide 49: References
Ablation test (VKI)
[1] Mikida, Cory, Andreas Klöckner, and Daniel Bodony. "Multi-rate time integration on overset meshes." Journal of Computational Physics 396 (2019): 325-346.
[2] Michalke, Alfons. "On the inviscid instability of the hyperbolic tangent velocity profile." Journal of Fluid Mechanics 19.4 (1964): 543-556.
[3] Blumen, William. "Shear layer instability of an inviscid compressible fluid." Journal of Fluid Mechanics 40.4 (1970): 769-781.
[4] Kozdon, Jeremy E., and Lucas C. Wilcox. "Stable coupling of nonconforming, high-order finite difference methods." SIAM Journal on Scientific Computing 38.2 (2016): A923-A952.

## Slide 50: BACKUP

## Slide 51: Gap: Attenuation
(Insert stuff here)

## Slide 52: Implementation: Code Generation
Ablation test (VKI)
(Insert text here)