## Slide 1: Time Integration of Reacting Flows and Energy-Stable Hybrid Spatial Discretizations
Cory Mikida (AE)
Preliminary Exam (Thursday, February 25th, 2021)

## Slide 2: Goals for This Presentation
Ablation test (VKI)

## Slide 3: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document

## Slide 4: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document
Expound upon certain aspects of both topics, namely current work

## Slide 5: Goals for This Presentation
Ablation test (VKI)
Fill in any “gaps” in the proposal document
Expound upon certain aspects of both topics, namely current work
More extensively motivate how I hope to spend the “best days of my life”

## Slide 6: Time Integration of Reacting Flows

## Slide 7: Motivation and Background
Ablation test (VKI)
LES Modeling of nine-species, nineteen-reaction hydrogen-air combustion mechanism. Source: NASA@SC12

## Slide 8: Motivation and Background
Ablation test (VKI)
Time integration of chemically reacting flows presents a significant set of simulation challenges
  Presence of stiff terms limits timestep – fluid-relevant timescale is much larger than reaction timescale
  Going fully explicit -> wasteful work
  Going implicit -> restrictive solve requirements
One common approach: operator splitting
What numerical tools exist that allow us to do better?

## Slide 9: Motivation and Background
Ablation test (VKI)
IMEX schemes, e.g. additive Runge-Kutta schemes of Kennedy and Carpenter
  Designed primarily for convection-diffusion-reaction equations
  Higher order (can be lost when simulating DAEs)
  Timestepping limitations removed, but timescales not easily split
Multi-rate schemes, e.g. multi-rate multistep schemes derived from Gear and Wells
  Splitting of timescales comes from per-component history management on different intervals
  Mixing of implicitly and explicitly advanced components not yet accomplished/unexplored

## Slide 10: Motivation and Background
Ablation test (VKI)
Given: an existing framework for multi-rate integration that has been proven effective for fully-explicit time advancement
  Timescale splitting -> apply CFL condition to overset meshes
  Component coupling -> energy-stable penalty-based interpolation
  Implementation: Python packages for code generation of multi-rate integrators as well as a number of other schemes, some of which are implicit/incorporate implicit solves
Consider: combining performance improvement capabilities of multi-rate integration with flexibility of treating different right-hand sides implicitly or explicitly

## Slide 11: Motivation and Background
Ablation test (VKI)
Potential impact: challenge existing state-of-the-art for CFD simulation of reacting flows -> produce faster and more accurate turnaround for…
  Combustion for propulsion: scramjets/ramjets
  Problems in atmospheric sciences -> climate concerns
  Furnaces/residential heating -> energy efficiency

## Slide 12: The Topic/Problem
Ablation test (VKI)
The mission statement: develop efficient, accurate, and stable time integration schemes for reacting flows
  Efficient: splitting of timescales via multi-rate
  Accurate and Stable: high-order temporal resolution, with flexibility to advance separate components implicitly or explicitly, as well as adaptivity introduced via local error-informed timestep control
Gauging efficacy: comparison with existing methods, stress-testing with appropriately stiff demonstrative problems

## Slide 13: Governing Equations
Ablation test (VKI)
Navier-Stokes equations with added equations for mass fraction evolution, as well as pressure/temperature evolution
In these equations:
𝜌 = density
ui = velocity in ith direction
𝛿ij = Kronecker delta
𝜏ij = fluid stress tensor
E = total energy
T = temperature
P = pressure
q = heat flux
Wk = molecular weight of kth species
ὠk = production rate of kth species
R = gas constant
n = number of moles of gas
[C]k = concentration of kth species
Cv,k = specific heat at constant volume of kth species
Uk(T) = internal energy of kth species at temperature T
Yk = mass fraction of kth species
𝜑ki = diffusion flux of kth species

## Slide 14: Governing Equations (2)
Ablation test (VKI)
Primary stiffness contribution is of course from the mass fraction evolution equations – in particular our focus is on RHS
Pressure and temperature updates typically come from energy relation/EOS:
For now, we instead adopt time rate of changes for these quantities based on operator-splitting approach (constant internal energy/volume in reaction substep)

## Slide 15: Gap: Species Production Rates
Ablation test (VKI)
Species production rates: Arrhenius rates

## Slide 16: Numerics: Multi-Rate Integration
Ablation test (VKI)
Solve y’ = a(t,y)…split into fast/slow terms
Multi-step methods: construct an approximation of a, ã based on history of past values
  Adams-Bashforth: construct ã using polynomial interpolation (explicit)
  For multi-rate: each a term in RHS has its own history, speed of evolution
yn+1 obtained by integrating ã
ã

## Slide 17: Numerics: Multi-Rate Integration (2)
Solve y’ = a(t,y)…split into fast/slow terms
Multi-step methods: construct an approximation of a, ã based on history of past values
  Adams-Moulton: construct ã using polynomial interpolation (implicit)
  For multi-rate: each a term in RHS has its own history, speed of evolution
yn+1 obtained by integrating ã
ã

## Slide 18: Numerics: Multi-Rate Integration (3)
Design choices for scheme synthesis include:
  Choice of timescale splitting – which components are fast-evolving, which are slow
  Step ratio
  Evaluation order: “fastest-first” vs. “slowest-first”
  When to re-extrapolate
  How much history to include: stability implication

## Slide 19: Gap: Multi-Rate Example
A walk-through of a macro-step with a simplified system…
Fastest-first scheme, step ratio H/h of 2
Step 1: Form polynomial extrapolants for both right-hand sides

## Slide 20: Gap: Multi-Rate Example (2)
Step 2: Integrate both extrapolants through one microstep
Step 3: Evaluate af at ti+1
Step 4: Update polynomial extrapolant for af to include new history

## Slide 21: Gap: Multi-Rate Example (3)
Step 5: Integrate fast extrapolant through one microstep; integrate slow extrapolant through one macrostep
Step 6: Evaluate af and as at ti+2
Step 7: Update polynomial extrapolants to include new history

## Slide 22: Numerics: Multi-Rate Integration (4)
Summary: reduction in total RHS evaluations is achieved by evaluating fast RHS twice as often as the slow RHS
  The key to the method is maintenance of histories at differing timestep intervals
  Initial histories are obtained via “bootstrapping” with Runge-Kutta methods of matching order
  Pictorial representations of macrostep process given in Kloeckner for a number of different configurations
What about application to chemistry/inclusion of implicit evaluation?

## Slide 23: Numerics: Multi-Rate Chemistry
Ablation test (VKI)
Revisit the governing equations: need to identify fast and slow components and coupling/self-influencing right-hand sides
Species production rates are a clear stiff/fast RHS, but what other state components depend on them directly?

## Slide 24: Numerics: Multi-Rate Chemistry (2)
With this possible splitting, right-hand side terms become:

## Slide 25: Numerics: Multi-Rate Chemistry (3)
Ablation test (VKI)
This is one possible setup, and its efficacy is currently undetermined
  Timescales of certain components and right-hand sides (energy, mass diffusion) somewhat unknown – mechanism specificity?
  Rates of coupling terms are a design choice to be determined
  Pressure and temperature right-hand sides still predicated upon operator splitting approach – their use will be clarified
Different splittings, step ratios, orders, schema are easily implemented via code generation approach (Leap, Dagrt)

## Slide 26: Numerics: Implicit Chemistry
Ablation test (VKI)
Given the stiffness of the chemistry that motivates this time integrator development, a natural inclusion in our framework is the ability to advance implicitly

## Slide 27: Numerics: Implicit Chemistry
Given the stiffness of the chemistry that motivates this time integrator development, a natural inclusion in our framework is the ability to advance implicitly

## Slide 28: Numerics: Implicit Chemistry (2)
Key need: Jacobian for the chemistry right-hand sides
  CVODE/operator-splitting approach uses a finite-difference Jacobian
  Being able to calculate actual Jacobian may have simulation value
  This motivates the selection of temperature and pressure right-hand sides based on an operator-splitting approach
PyJac-V2: code generation of source terms and Jacobians

## Slide 29: Numerics: Implicit Chemistry (3)
Some important distinctions:
  PyJac-V2 implements equations that assume a reaction substep model, taking either constant-pressure/enthalpy or constant-volume/internal energy
  For the time being we are using the latter
  PyJac-V2 also implements the equations using the number of moles of each species as the independent variables
Constant-Volume
Constant-Pressure

## Slide 30: Numerics: Implicit Chemistry (4)
Critical consideration: ideal gas law drift
  Time-integrating the temperature and pressure differentials no longer rigorously enforce algebraic constraints (constant internal energy, ideal gas law)

## Slide 31: Numerics: Implicit Chemistry (5)
To mitigate this: Jacobian modification
  Removes pressure and temperature rows/columns
  Incorporates constant internal energy constraint into species elements
  Pressure and temperature can then be updated algebraically
Additional option: RHS penalization (attenuation)

## Slide 32: Gap: PyJac-V2 Validation
Some preliminary work – validating PyJac correctness
  Source terms: direct comparison w/Cantera (San Diego)
  Jacobian: check convergence to 2nd order w/centered FD

## Slide 33: Gap: PyJac-V2 Validation
Some preliminary work – validating PyJac correctness
  Source terms: direct comparison w/Cantera (San Diego)
  Jacobian: check convergence to 2nd order w/centered FD

## Slide 34: Gap: PyJac-V2 Validation
Some preliminary work – validating PyJac correctness
  Source terms: direct comparison w/Cantera (San Diego)
  Jacobian: check convergence to 2nd order w/centered FD

## Slide 35: Gap: PyJac-V2 Validation
Some preliminary work – validating PyJac correctness
  Source terms: direct comparison w/Cantera (San Diego)
  Jacobian: check convergence to 2nd order w/centered FD

## Slide 36: Numerics: Error/Timestep Control
Motivation: reacting flow simulations, especially featuring ignition, often feature stretches of near-equilibrium chemistry punctuated by temperature/mass fraction spikes
  Timestep requirements for stability/accuracy naturally vary

## Slide 37: Numerics: Error/Timestep Control (2)
Ablation test (VKI)
CVODE accounts for this by obtaining a local truncation estimate using state calculations at two differing orders – we match this approach
  Similar to ODE23/ODE45 timestep adaptors, but uses weighted RMS norm to handle states with components widely varying in magnitude
  State calculations for Adams methods: carry extra history value
|E|>1
|E|<1

## Slide 38: Numerics: Error/Timestep Control (3)
Ablation test (VKI)
Design choices inherent to this approach:
  How often to adapt the timestep (micro- vs. macrostep checks)
  Error norm/adapting controller to stiffness-related situations (later)
  Which state components should be included when
  Timestep adaptivity vs. step ratio adaptivity
|E|>1
|E|<1

## Slide 39: Current Status: Controller
Ablation test (VKI)
Applying fully explicit (adaptive) integration to stiff Cantera example problem to stress-test controller

## Slide 40: Current Status: Controller (2)
Ablation test (VKI)
Applying fully explicit (adaptive) integration to stiff Cantera example problem to stress-test controller
Governing equations do not allow for PyJac intervention
Ablation test (VKI)
Reactor 1
Reactor 2

## Slide 41: Current Status: Controller (3)
Ablation test (VKI)
Applying controller to known methods (namely embedded RK – ODE23) shows timestep “jitter” near chemical equilibrium
  Floating-point issues/cancellation – documented by PyJac
  Use of Scipy implementation confirms this result
  Can we design a controller for integration that alleviates this?
Ablation test (VKI)
Ablation test (VKI)
Leap

## Slide 42: Current Status: Controller (3)
Ablation test (VKI)
Applying controller to known methods (namely embedded RK – ODE23) shows timestep “jitter” near chemical equilibrium
  Floating-point issues/cancellation – documented by PyJac
  Use of Scipy implementation confirms this result
  Can we design a controller for integration that alleviates this?
Ablation test (VKI)
Ablation test (VKI)
Leap
Scipy

## Slide 43: Demonstrative Test Problem
Ablation test (VKI)
Target application: reacting mixing layer
  Fundamentally-driven model of combustion for propulsion
  Twistable speed knobs: crossflow magnitude (fluid), Arrhenius pre-exponential factors (chemistry)
Baseflow: hyperbolic tangent velocity profile
  San Diego 9-species ideal gas mixture
  Ignition localized to mixing layer via introduction of temperature variation

## Slide 44: Current Status: Test Problem
Ablation test (VKI)
Establishing initial perturbation and subsequent growth rate that matches literature using linear stability theory

## Slide 45: Current Status: Test Problem
Growth rate calculations from PC2 solution use vertical velocity (no baseflow magnitude)
Formula derived from assumption that wave disturbances go like (from Blumen)
Ablation test (VKI)
Establishing initial perturbation and subsequent growth rate that matches literature using linear stability theory

## Slide 46: Current Status: Synthesis/V+V
Ablation test (VKI)
In the midst of multi-rate Adams development, implicit chemistry framework can be tested with schema existing in Leap
Generate code for chemical source terms, Jacobian, and IMEX ARK4 integration (K+C), and ”wire in” to fluid solver (PlasCom2)
Ensure that we have…

## Slide 47: Current Status: Synthesis/V+V
…design-order convergence for a homogeneous autoignition example (9-species San-Diego mechanism)

## Slide 48: Current Status: Synthesis/V+V
Ablation test (VKI)
…design-order convergence for a homogeneous autoignition example (9-species San-Diego mechanism) ✓
EOC: 3.89
But: case does not contain meaningful fluid motion (single-pt)
Uses Jacobian modified for explicit constraint enforcement

## Slide 49: Current Status: Synthesis/V+V
Ablation test (VKI)
…good agreement with laminar flame speed returned by steady-state Cantera analysis for a freely propagating flame example✓
To-do: design order convergence in this case?

## Slide 50: Risk Mitigation
Ablation test (VKI)
Important question: what if this doesn’t work out?
  Reinforces CVODE as state-of-the-art for implicit treatment of chemical kinetics
  Fallback: exploration of effect of analytical Jacobian versus finite difference Jacobian. Convergence effects? Performance effects?
  Fallback: controller improvement. Tailoring to kinetics/mechanism?
  Fallback: other target applications for implicit-explicit multi-rate
Actionable response: frontload controller design, Jacobian implementation/verification using simple(r) problems

## Slide 51: Outlook and Open Questions
Ablation test (VKI)
Quantifiably characterizing benefit of analytical versus finite-difference Jacobian
  Accuracy and time-to-solution (fewer implicit solve iterations)
  Rigorously test effect(s) of constant-volume assumption for Jacobian
Develop error/timestep control algorithm with more robustness in the face of near-equilibrium floating point issues
Establish timescale splitting for full governing equations
Explore (large) design space
  Implicit-explicit multi-rate framework
  Timestep control algorithm also has “knobs” to turn

## Slide 52: Energy-Stable Hybrid Spatial Discretizations

## Slide 53: Motivation and Background
Ablation test (VKI)
Flow simulations incorporating complex geometries present obvious meshing challenges
Accuracy and stability can be affected by poor mesh quality

## Slide 54: Motivation and Background
Ablation test (VKI)
One common approach: finite difference discretization(s) with some consideration for meshing near trouble regions
  Curvilinear meshes w/coordinate transforms
  Overset meshes
  Multiblock

## Slide 55: Motivation and Background
Ablation test (VKI)
Within the multiblock approach, one can opt for conforming or nonconforming interfaces between blocks
  The latter provides more flexibility but arguably requires more thought

## Slide 56: Motivation and Background
Ablation test (VKI)
Recent body of existing work in nonconforming interfaces, specifically w.r.t. summation-by-parts finite difference discretizations, is large
  Mattsson and Carpenter (2010): fixed refinement ratio, matching corners
  Nissen et al. (2015): matching corners
  Kozdon and Wilcox (2016)
  Friedrich et al. (2018): degree-preserving
  Almquist et al. (2019): (better) degree-preserving
But: can we obtain more flexible methodology?

## Slide 57: Motivation and Background
Ablation test (VKI)
Another way: establish nonconforming interface between structured (SBP) and unstructured (DG) discretizations
  Nordstrom and Gong (2006): low-order FD-FV
  Kozdon and Wilcox (2016): (same work as previous slide) – establishes provably stable interface for nonconforming interfaces between SBP discretizations and between SBP-DG discretizations, but has a number of failings
We ask (again): can we do better?

## Slide 58: The Topic/Problem
Ablation test (VKI)
The mission statement: develop energy-stable and high-order accurate interface(s) between structured (SBP) and unstructured (DG) spatial discretizations
  Remove underdetermined elements of interface construction
  Stretch goal: establish fidelity in round-trip projection
  Above all: do not sacrifice provable stability

## Slide 59: Motivation and Background
Ablation test (VKI)
Potential impact: remove troublesome geometric constraints on existing simulations, while also
  Introducing ability to more readily introduce a certain discretization to a certain portion of the spatial domain
  Flexible and selective application of beneficial properties of a given method to ”trouble spots” – e.g. shocks

## Slide 60: In This Section…
Ablation test (VKI)
I will be approaching this section of the talk a bit differently
Whereas the document provides a lot of the background detail on the separate discretizations/lays the groundwork for the target problem, the talk will focus more on the state of the interface
In particular, my goal is to demonstrate its weaknesses

## Slide 61: Governing Equations
Ablation test (VKI)
Nonetheless, the governing equations we initially target will be used later, so they deserve mention
As with K+W, first-order wave equation in two dimensions
Worth noting: the hope is to ultimately extend interface method to
  Higher dimensions
  Different problems

## Slide 62: Demonstrating Stability
The golden rule: fully characterize an interface that is energy-stable
How to describe the energy dissipation rate at edges on the interface?
Total Energy
Per-Block
DG
SBP

## Slide 63: Demonstrating Stability
Skipping over a lot of detail here, but:
Key question from here: how do we define starred quantities such that these quantities can be proven to be non-positive?
  DG: numerical fluxes
  SBP: SAT penalty terms
DG
SBP

## Slide 64: Interface Method
This is where the interface comes in
Top-level characterization of interface: operators that project Grid A solution to Grid B (and vice versa)
Starting point for describing P: Kozdon and Wilcox
  Approach has qualities we want to retain, namely energy-stability applicable to both nonconforming SBP interfaces and hybrid interfaces

## Slide 65: Interface Method: Glue Grids
Primary mechanism: projecting nodal solutions (on grids) to intermediate “glue” grid
  Solution on glue grid described by modal coefficients multiplying Legendre polynomials defined on [-1,1]
  What results: piecewise continuous polynomial representation
Projection is then fully described by “glue-to-grid” and “grid-to-glue” operators

## Slide 66: Interface Method: Glue Grids
Critical note: product of these operators is NOT assumed to be identity
  Recall desire for “round-trip” projection fidelity – is this possible?
Before delving further into construction, we need to revisit the energy dissipation rates and insert definitions of interface quantities that use this nomenclature
  What condition(s) for stability “pop out?”

## Slide 67: Interface Method: Flux/Penalty
What will make this easier: a visual representation of one potential target simulation
  Box domain split in half in x – left half employs SBP finite-difference, right half uses DG

## Slide 68: Interface Method: Flux/Penalty
For a conforming SBP interface, an energy-stable definition of the SAT penalty term can be given as
Linear combination of combination of central and upwind penalties (𝜶 controls “upwindedness”)
Nonconforming interface relies on a similar principle, with the discretizations conforming at the glue-grid level

## Slide 69: Interface Method: Flux/Penalty
We can describe the same penalization on the glue grid using glue grid quantities (barred):
Glue grid quantities are projected from the grid to the glue using the aforementioned operators:

## Slide 70: Interface Method: Flux/Penalty
Note that surface Jacobians are also projected, along with a scaling factor

## Slide 71: Interface Method: Flux/Penalty
What remains: describing SAT penalization on the grid using the glue grid penalization
  Recall: projection error is nonzero
  For now – assume SBP block covers entire glue grid interface (no 𝚫)

## Slide 72: Interface Method: Flux/Penalty
Similarly, for a single element of DG:
  No projection error – set glue space to be higher-order space than DG
Plugging these fluxes and penalties back into the edge dissipation rates provides a condition for non-positivity

## Slide 73: Interface Method: Compatibility
The compatibility condition is what allows for provable energy stability
  (Lengthy) proof given in Kozdon and Wilcox
  Critical question: dependence on assumptions/specific formulation/governing equations?
Given its importance, this condition is considered to be an explicit constraint when constructing the operators

## Slide 74: Gap: Glue-to-Glue Projection
Note: for misaligned grids, or grids with different order of accuracy, multiple glue layers are needed
Provided glue-to-glue projections satisfy their own version of compatibility, we can assume Pf2g projects to the finest layer without loss of generality

## Slide 75: Interface Method: Construction
We will go through the basics of the operators construction and identify areas of exploration/improvement
Solution description on glue grid: piecewise continuous polynomials
𝝓: [-1,1] Legendre polynomials shifted to interval k

## Slide 76: Interface Method: Construction
In the interior, assume a symmetric operator, and assume a stencil like this:
Stencils inspired by SBP interior construction

## Slide 77: Interface Method: Construction
Interior and boundary order pairs match SBP as well
m = 2l
What conditions do we want to enforce in either direction with this stencil?

## Slide 78: Interface Method: Construction

## Slide 79: Interface Method: Construction

## Slide 80: Interface Method: Construction
What results (in the interior) is in actuality an overconstrained system

## Slide 81: Interface Method: Construction
Furthermore, an additional constraint is fulfillment of the compatibility condition
In practice, Kozdon and Wilcox solve for one projection operator (glue-to-grid), and obtain the other via the above condition
Major question: why are point constraints also fulfilled?

## Slide 82: Interface Method: Construction
Meanwhile, what about the stencil/constraints near the boundary?
  As with SBP, lower order of accuracy enforced
(r)
(s+1)

## Slide 83: Interface Method: Construction
Given the lower order enforced, as well as the expanded stencil, this is where the DOFs outstrip the constraints in total
Stencil shape and order constraints again inspired by SBP, and likely dictated by compatibility

## Slide 84: Interface Method: Construction
Final operator solve is underdetermined
System closed by optimizing to bring the product of the projection operators closer to an identity
  Minimize distance between nearest eigenvalues
Implication: there is more that we can ask for

## Slide 85: Interface Method: Construction
Further evidence of this: applying the SBP4-2 inspired projection to an SBP-to-SBP projection of a sine wave shows high errors/unsavory behavior at boundaries

## Slide 86: Interface Method: Construction
Additional experiment: what if we turn off the optimization and look at the result of the constraint solve?
  Sparsity patterns at higher orders near boundary somewhat baffling
  Optimization does not move character of operators far from this point

## Slide 87: Interface Method: Construction
Main takeaway: construction can be improved
  Constraint/compatibility solve gives an unintuitive result
  We should strive to remove any optimization
  Experimentation with changes in DOF pattern, additional constraints
  Modifying polynomial description on the glue grid
  Cannot change this at the cost of stability
Current approach: initial focus should be on interior
  Far simpler, and has its own set of questions
  How does compatibility influence the stencil?
  What does solving for one operator and using compatibility to obtain the other say about the accuracy of each?

## Slide 88: Current Status: Understanding the Interior
One useful way to explore this: fully periodic SBP-to-SBP advection example
Does compatibility condition provide the same energy stability in this case as in the first-order wave equation?
A walkthrough of this example follows

## Slide 89: Current Status: Advection Demo
Insert “glue” layer into a periodic domain
  Can we prove energy stability with existing operators/compatibility?
Glue Grid
  Condition on 𝝉?

## Slide 90: Current Status: Advection Demo
Without the glue grid, the two sides of the domain conform at the grid point level, and proof of stability follows from energy:

## Slide 91: Current Status: Advection Demo
With the glue grid involved, we must examine the penalization on the glue grid interval level

## Slide 92: Current Status: Advection Demo
From there, use compatibility:
This gives the same condition on 𝝉 as before, via the same analysis of principal minors to prove negative semi-definiteness

## Slide 93: Current Status: Advection Demo
Validate this approach by both confirming energy ODE matches evolving energy of integrated system, and by confirming that for 𝝉 = 1, system energy decreases
Glue Grid

## Slide 94: Current Status: Advection Demo
Main takeaway: keys to provable stability are use of compatibility to express energy on the glue grid level only, as well as clever “error” definition
Glue Grid

## Slide 95: Demonstrative Test Problem
Ablation test (VKI)
Initial target is the same as Kozdon and Wilcox, with split domain previously shown
(IC)

## Slide 96: Demonstrative Test Problem
Ablation test (VKI)
Initial target is the same as Kozdon and Wilcox, with split domain previously shown
(Soln.)

## Slide 97: Risk Mitigation
Ablation test (VKI)
Important question: what if this doesn’t work out?
Still to-do with existing operators: extension to three dimensions/additional problems
  Susceptibility to geometric corner cases?
  Does compatibility condition universally provide stability?
Additional question: effect on time integration
  Stiffness of interface projection relative to interior/exterior boundaries
  Exposure to multi-rate as needed would be straightforward

## Slide 98: Outlook and Open Questions
Ablation test (VKI)
Currently: projection operator approach implemented in Python SBP-DG hybrid code
  Assessed via advection and wave examples
Various concerns raised
  Optimization to “close the loop” should be avoided
  Sparsity of projection operators, as well as boundary behavior, is troubling
  Constraints outlined in literature are in practice ignored
Critical and continuing question: how can we improve this formulation?
  Additional constraints/fewer DOFs?
  Rethinking compatibility as a critical condition?

## Slide 99: References
Ablation test (VKI)
[1] Mikida, Cory, Andreas Klöckner, and Daniel Bodony. "Multi-rate time integration on overset meshes." Journal of Computational Physics 396 (2019): 325-346.
[2] Michalke, Alfons. "On the inviscid instability of the hyperbolic tangent velocity profile." Journal of Fluid Mechanics 19.4 (1964): 543-556.
[3] Blumen, William. "Shear layer instability of an inviscid compressible fluid." Journal of Fluid Mechanics 40.4 (1970): 769-781.
[4] Kozdon, Jeremy E., and Lucas C. Wilcox. "Stable coupling of nonconforming, high-order finite difference methods." SIAM Journal on Scientific Computing 38.2 (2016): A923-A952.

## Slide 100: BACKUP

## Slide 101: Gap: Mass Diffusion
Ablation test (VKI)
Mass diffusion: mixture-averaged model with correction term for mass conservation
Xk: mole fraction of species k, W: mean molecular weight, Dk,m: binary diffusivity coefficient
How stiff is this relative to the species production rates?

## Slide 102: Gap: Thermodynamic Quantities
Ablation test (VKI)
Various thermodynamic quantities for gas mixtures: NASA 9-coefficient polynomial characterization
  Unlike NASA7, supports arbitrary number of temperature regions
  More accurate in cases with large temperature variation
Used to produce per-species descriptions of internal energy and specific heats at constant volume
Totals for mixtures can be obtained using these quantities in conjunction with species concentrations

## Slide 103: Gap: Attenuation
(Insert stuff here)

## Slide 104: Implementation: Code Generation
Ablation test (VKI)
(Insert text here)